## Slide 1
Air pollution source term estimation
using self-adaptive Evolutionary multiobjective optimization
Shai Kendler#,1,2, Idit Belachsen1, Asaf Nebenzal3, David Gold4, Patrick. M. Reed4, Barak Fishbain1
Dept. of Environmental, Water and Agricultural Engineering, Faculty of Civil & Environmental Engineering, Technion – Israeli Institute of Technology, 2. Environmental physics department, Israel Institute for Biological Research, 3. Department of Mathematics, Technion – Israel Institute of Technology, 4. School of Civil and Environmental Engineering, Cornell University
# Corresponding authors: Prof. Shai Kendler - ikendler@gmail.com, Asaf Nebenzal - asaf.n@technion.ac.il
Results
Introduction
This work was partially supported by the Israeli Ministry of Science and Technology
Research program.
Conclusions
Methodology
What are Evolutionary Algorithms (EAs)?
Source term estimation
Research objectives
What is multi-objective optimization?
Objective-1:
Minimize the difference between
sensors’ actual and computed readings:
Source term estimation is a crucial step in assessing the pollution dense map and the resulted impact on the environment.
These tasks get complicated as the number of possible leaks increases and the number of sensors decreases.
The use of a multiobjective optimization approach was proven to be effective, as it enables balancing between the error of the estimated contamination level and simplicity (following Occam’s razor principle of parsimony).
The resulted simplicity-accuracy tradeoff function (the Pareto frontier) can be used by decision-makers to handle the complicated situation of a source with multiple leaks.
Using a WDESN, comprised of portable and low-cost Micro Sensing Units (MSUs), that can measure, process and transmit data, provides the opportunity to monitor large areas at a reasonable cost.
Nevertheless, to obtain an optimal deployment of such network, the varying meteorological conditions, the sensor attributes, the fiscal constraints and many other parameters should be considered.
As part of our on-going research, the PED criteria, presented in this work, will be used along with other conflicting objectives to retrieve the optimal deployment configuration in time and space of a WDESN.
A leak of various chemicals from
industrial activity may harm humans
and the environment.
The first line of defense is detection
of the resulted plume and mapping
the contamination level.
Large number of sensors are typically
needed for achieving concentration maps of high spatial and temporal resolution.
An alternative approach is to locate the leak source and flow rate (i.e., source term), and use it as input to an atmospheric dispersion model to generate spatial dense pollution maps.
To estimate the source term in the case of multiple leaks and a sparse Wireless Distributed Environmental Sensor Network (WDESN), using state-of-the-art optimization technique - the Borg Multi-Objective Evolutionary algorithm (MOEA) framework, coupled with a Gaussian plume dispersion model.
More than one objective function is optimized simultaneously, creating tradeoffs between conflicting objectives, such as - error rate and cost (Fig. 2).
A Pareto frontier is the set of non-dominated solutions, being chosen as optimal, if no objective can be improved without harming at least one other objective.
Problem formulation
Figure 3. A general scheme of an Evolutionary Algorithm
Figure 5. Pareto frontiers calculated for the “Co9/9” arrangement for several .
Figure 6. A comparison between the calculated and the actual leak rate in “Co9/9” arrangement for several .
Figure 7. Color map for calculated PED as a function of . a) “L9/9”, b) “Co9/9”, c) “Co9/6”, d) “L9/6”. Figures are truncated at , to allow comparison complex and simple situations
Figure 1. Example of a source and a network of sensor (﻿Hutchinson et. al., 2017).
600*600 m2 flat area
Constant west-wind (5 m/s)
Slightly unstable conditions
Leak rates of 0-1000 kg/s
Varying number of leaks (0-9)
Leak heights of 5m AGL
Figure 4. Source-sensors arrangements.
a). ("Co9/9") - compact group 50m apart,
b). (”L9/6") - same as “Co9/9”, using 6 sensors,
c). (”L9/6") - a line of 6 sensors 50m downwind,
d). (”L9/9") - a line of 9 sensors 50m downwind.
  Figure 5 shows the Pareto frontiers calculated by the Borg for the “co9/9” arrangement, for an increasing number of leaks, .
  The minimum is achieved for the correct number of leaks.
  Figure 6 shows a comparison between the preset leak rates and the calculated leak rates
  Excellent agreement is seen, due to the relatively convenient sensing configuration.
Scenario-complexity
estimation
  PED = Pairwise Euclidean Distance is defined as:
  for the network observed readings between two sets of active sources with different sizes {S}’ and {S}”.
  Figures 7a and b exhibit high PED values (yellow) = simple scenarios
  Figures 7c and d exhibit low PED values (blue) = complex scenarios
Figure 2. Example of tradeoff between two objectives and the Pareto frontier
Non-dominated
Solution
Dominated
solution
Pareto frontier
A set of candidate solutions
All solutions are Non-dominated
Environmental pressure causes natural selection. Better candidates are more likely to survive and reproduce
New
solutions
Objective-2:
Minimize the number of
active sources (NAS):
Simulation set
Future work
Acknowledgements