## Slide 1: Development of methods for adaptive and optimal deployment of heterogeneous sensor array for accurate representation of air pollution and its sources
1/27
Pre-Thesis seminar - 7.8.2019
Idit Belachsen
Advisors: Associate Professors - Barak Fishbain, Shai Kendler

## Slide 2
Introduction - air pollution monitoring (motivation), representation in time and in space, network deployment
Research hypothesis and objectives
Related work
Methods – background (Meteorology, Evolutionary Algorithms, Borg), problem formulation
Preliminary results
Summary and research plan
Table of contents

## Slide 3: Air pollution monitoring
Major pollutants – NoX, CO, CO2, SO2, O3, BC, other PM
The main incentive for air pollution monitoring:
Emission control
Short-term - prevent population exposure, regulatory enforcement
Long-term – epidemiological or climate research, planning
Major challenge – producing high resolution pollution concentration maps, using the current monitoring methods
Wireless Distributed Environmental Sensor Network (WDESN)
Portable and relatively low-cost Micro Sensing Units (MSUs)
Introduction

## Slide 4: Representation in time and in space
IDW, KRIGING interpolation, LUR models
Atmospheric Transport and Dispersion (ATD) models
Knowledge on weather, location and quantity of the released pollutant is needed for ATD. If absent – STE can be applied
Introduction
﻿Hutchinson et. al., 2017

## Slide 5: Network deployment
Introduction
A new challenge is formed – what is the best way to deploy a network of sensors?
If resources are unlimited, the task is easy
The cost of a network is determined by – number of sensors and their attributes (sensitivity, dynamic range)
Practical considerations constrain some locations
Static deployment Vs. dynamic deployment
5
Introduction

## Slide 6: Network deployment
The basic problem is equivalent to the “0-1 knapsack” problem:
Given a set of n items, ﻿each of which has some value and some cost , how do we select a subset of those items that maximizes the value while keeping the summed cost within some capacity ?
Candidate solutions can be represented as binary array of length n (1 = an item is included in the knapsack / a sensor is placed in that position, 0 = the item is omitted / the sensor is not placed)
The solution-space size is then 2n and the problem is NP-hard = the time required to solve the problem, using any currently known algorithm, increases rapidly as the size of the problem grows.
approximation algorithms are required beyond a certain size of problem.
Introduction
Notes: אז איזה עבודות נעשו עד כה בתחום ?
לא מעט עבודות הגיעו מרקע של מדעי המחשב, או מעולם החיישנים בכלל, ללא ספציפיות לזיהום אוויר.
מקריאה של מאמרים בתחום, אני חושבת שהיה ברור שיש קשר בין השיטה שיושמה לבין המטרה או השימוש של הרשת אותה רצו לפרוש.
כלומר -
להוסיף כאן את הנאפסק פרובלם. בעיית תרמיל הגב. בגלל שזו בעיה שקולה, הרבה מהניסיונות הם מתחום מדעי המחשב
As the basic problem of sensors’ optimal deployment aims at maximizing the utility of the network, while minimizing its cost, the problem is equivalent to the “0-1 knapsack” problem [29], [40], where a subset of items out of n items, possessing each some value 𝑣_𝑖 and some cost 𝑐_𝑖, are selected so values’ sum is maximized, while the summed cost is kept within some capacity 𝑐_𝑚𝑎𝑥.
In both problems, candidate solutions can be represented as binary strings of length n, where a 1 in a given position indicates that an item is included in the knapsack, or that a sensor is placed in that position, and a 0 indicated the item is omitted, or the sensor is not placed. The solution-space size is then 2n. This basic problem is NP-hard [41], meaning that the time required to solve the problem, using any currently known algorithm, increases rapidly as the size of the problem grows. As a result, approximation algorithms, which focuses on finding good solutions (“global optimums”) instead of provably optimal solutions, are required beyond a certain size of problem.
Global optimization refers to the process of attempting to find the solution 𝑥^∗, out of a set of possible solutions {𝑋}, that has the optimal value for some fitness function f, such that 𝑥≠𝑥^∗→𝑓(𝑥^∗ )≥𝑓(𝑥) [42]. Two main categories of methods to find 𝑥^∗ exist; the first are deterministic methods, which find 𝑥^∗ by an exhaustive search over the set {𝑋}. Stochastic methods involve random elements that try to reduce the computational burden of pure random search. ﻿At the outset, a random sample of points in the set {𝑋} is picked. Then, each method manipulates the sample points using different heuristics, which are sets of rules for deciding which potential solution out of {𝑋}"should next be generated and tested [43]. Local search algorithms (often referred to as hill climbers), work by taking a starting solution x, and then searching"set {𝑋}

## Slide 7: Research hypothesis
An optimal deployment of a WDESN is required for the purpose of:
obtaining early warnings when an increase in industrial gas emission occurs
generating pollution dense maps
A set of optimal deployment solutions can be retrieved using multi-objective optimization techniques that balance between detection capabilities of the network and operational requirements.

## Slide 8
General | Specific
To design and develop a decision-making tool for an optimal deployment in time and in space of heterogenous sensor array, that will allow decision-makers to discover tradeoffs between performance criteria and to consider alternative modes of action that may not have been apparent prior to the analysis. | Design an optimization model, comprised of the following modules:
 | A spatial optimization model A temporal optimization model A spatial-temporal optimization model
 | Consider: various sources/sensors configurations, weather conditions and emission rates, heterogenous network, case-study of real-world
Research objectives
8

## Slide 9: Related work
The designated applications determines the goal that guides the optimization process. For example:
  Population exposure assessment (Kanaroglou et al., 2005)
  Threshold crossings detection (Boubrima et al., 2017)
  Improve existing network performance (Berman et al., 2019)
Knowledge gaps
Predefined number of air pollution sensors
Relied on existing measurements from monitoring stations (instead of using a dispersion model)
Assumed a decay with distance from a pollution source
Ended up placing sensors at the highest mean pollution zones
Notes: אז איזה עבודות נעשו עד כה בתחום ?
לא מעט עבודות הגיעו מרקע של מדעי המחשב, או מעולם החיישנים בכלל, ללא ספציפיות לזיהום אוויר.
מקריאה של מאמרים בתחום, אני חושבת שהיה ברור שיש קשר בין השיטה שיושמה לבין המטרה או השימוש של הרשת אותה רצו לפרוש.
כלומר -
להוסיף כאן את הנאפסק פרובלם. בעיית תרמיל הגב. בגלל שזו בעיה שקולה, הרבה מהניסיונות הם מתחום מדעי המחשב
As the basic problem of sensors’ optimal deployment aims at maximizing the utility of the network, while minimizing its cost, the problem is equivalent to the “0-1 knapsack” problem [29], [40], where a subset of items out of n items, possessing each some value 𝑣_𝑖 and some cost 𝑐_𝑖, are selected so values’ sum is maximized, while the summed cost is kept within some capacity 𝑐_𝑚𝑎𝑥.
In both problems, candidate solutions can be represented as binary strings of length n, where a 1 in a given position indicates that an item is included in the knapsack, or that a sensor is placed in that position, and a 0 indicated the item is omitted, or the sensor is not placed. The solution-space size is then 2n. This basic problem is NP-hard [41], meaning that the time required to solve the problem, using any currently known algorithm, increases rapidly as the size of the problem grows. As a result, approximation algorithms, which focuses on finding good solutions (“global optimums”) instead of provably optimal solutions, are required beyond a certain size of problem.
Global optimization refers to the process of attempting to find the solution 𝑥^∗, out of a set of possible solutions {𝑋}, that has the optimal value for some fitness function f, such that 𝑥≠𝑥^∗→𝑓(𝑥^∗ )≥𝑓(𝑥) [42]. Two main categories of methods to find 𝑥^∗ exist; the first are deterministic methods, which find 𝑥^∗ by an exhaustive search over the set {𝑋}. Stochastic methods involve random elements that try to reduce the computational burden of pure random search. ﻿At the outset, a random sample of points in the set {𝑋} is picked. Then, each method manipulates the sample points using different heuristics, which are sets of rules for deciding which potential solution out of {𝑋}"should next be generated and tested [43]. Local search algorithms (often referred to as hill climbers), work by taking a starting solution x, and then searching"set {𝑋}

## Slide 10: Methods - background
Methods
Optimization
Connect between emissions and predicted concentrations
What models exist?
The Gaussian plume model
Atmospheric Transport and Dispersion (ATD) model
Relevant meteorological parameters
Meteorology
What is multi-objective optimization?
What are Evolutionary Algorithms?
What is the Borg Framework?

## Slide 11: ATD models
Methods
Types: box models, Gaussian plume models, Lagrangian models, Eulerian dispersion models, Dense gas models
The Gaussian plume model - analytical steady state solution to the advection-diffusion equation for idealized circumstances
Q [kg s-1] = release rate from the stack, H [m] = effective height (actual stack height h + plume rise h)
x, y and z [m] = downwind, crosswind and vertical distances, [m s-1] = mean wind speed,
and [m] = represent the standard deviation of the Gaussian concentration distribution
Notes: The term dispersion is comprised of diffusion (due to turbulent eddy motion) and advection (due to wind) that occurs within the air near the Earth’s surface [18]. ATD models can forecast the spread of the pollutants, when available results from monitoring data are used for calibration and evaluation of model performance.
Several types of fundamental dispersion models exist: box models, Gaussian plume models, Lagrangian models, Eulerian dispersion models and Dense gas models as well as extensions and combinations of all of the above
Several simplifying assumptions are made in order to reach the Gaussian plume model equation (Eq. 1) [18]:
The pollutant is emitted in a constant rate Q from a single point source located at height H above ground surface.
The wind velocity is constant and aligned with the positive x-axis.
The solution is steady state.
The eddy diffusion coefficient K [m2 s-1] is a function of the downwind distance x only, and diffusion is isotropic so that 𝐾_𝑥 (𝑥)=𝐾_𝑦 (𝑥)=𝐾_𝑧 (𝑥)=:𝐾(𝑥).
Wind velocity is sufficiently large that diffusion in the x-direction is much smaller than advection.
Variations in topography are negligible so that the ground surface can be taken as the plane z=0.
The pollutant does not penetrate the ground.
To these assumptions we add that the material diffused is non-reactive in the atmosphere, with a negligible deposition rate and that background pollution is negligible as well. 𝜎 parameters are used instead of the eddy diffusion coefficient 𝐾(𝑥), due to the fact that they are much easier to determine experimentally and can usually be described by a simple power law of the form:
𝜎_𝑦=𝑎𝑥^𝑏
(2a)
𝜎_𝑧=𝑐𝑥^𝑑+𝑓
(2b)

## Slide 12: Main model assumptions
The solution is steady state.
The wind velocity is constant and aligned with the positive x-axis.
Variations in topography are negligible so that the ground surface can be taken as the plane z=0.
The pollutant does not penetrate the ground.
The material diffused is non-reactive in the atmosphere, with a negligible deposition rate
Background pollution is negligible
Methods

## Slide 13: Meteorology
The meteorological parameters that play a role in any gas dispersion model are wind speed, wind direction, and the atmospheric stability condition.
Methods
﻿Ahrens and Henson, 2017

## Slide 14: Multi-objective optimization
More than one objective function is optimized simultaneously, creating tradeoffs between conflicting objectives, such as - error rate and cost.
A Pareto frontier is the set of non-dominated solutions, being chosen as optimal, if no objective can be improved without harming at least one other objective.
Hadka (2017)
Non-dominated
Solution
Dominated
solution
Pareto frontier
Methods

## Slide 15: Evolutionary Algorithms
A set of candidate solutions
All solutions are Non-dominated
Environmental pressure causes natural selection. Better candidates are more likely to survive and reproduce
New
solutions
Eiben and Smith (2007)
Methods

## Slide 16: Borg MOEA
Methods
Hadka (2013)
Developed by David Hadka and Patrick Reed
Classified as a hyper-heuristic global multi-objective search tool
Uses internal feedbacks to dynamically adapt an ensemble of genetic recombination operators

## Slide 17: Problem formulation - notation
- region of interest (the industrial area and its surroundings) where we wish to place our network of sensors at.
- the set of sources. Each source, is located in and for a specific time t, emits [kg s-1].
- the set of sensors. Each sensor, , is located in and records a pollution level of .
Methods
Notes: The location of the sources 〖{ω〗_s} are known, these are the locations of the industrial plants.
For multiple sources scenario, each sensor readings are simply the sum of all sources’ contributions, which are the sources’ emissions multiplied by their corresponding transfer function, 𝑚_𝑠𝜔, i.e.:
As each source owns its unique parameters and location with respect to the sensors, the values of m_sr for each source-sensor combination is determined by the dispersion model, such as the Gaussian plume model.
כרגע אני אתייחס לניסוח הבעיה הראשונה – שהיא הבעיה שהגדרתי עד כה.

## Slide 18: Problem formulation - PED
Main goal: finding an optimal deployment (number and locations) of a set of sensors , considering a set of potential positions in the region of interest, so a possible increase in industrial gas emissions is more likely to be detected and the source-term estimation problem is more likely to be resolved.
Pairwise Euclidean Distance (PED) - a criterion that incorporates the sensitivity of the deployed network to changes in the source term.
Methods
Notes: Technically, we assume that each location ω∈Ω may host a sensor. The decision variables are held in a data array, each value represents a sensor, linked to a certain location ω∈Ω. The sensor is “placed” in that location if the decision variable is 1 and is not “placed” if the decision variable is 0.
הקריטריון מחשב מרחק אוקלידי בין קריאות החיישנים של שני סטים שונים של מקורות בעלי מספר שונה של מקורות פעילים – מסומן ב-S’ ו-S’’.
רשת חיישנים שרגישה לשינויים בפליטות המקור תיצור ערכי PED גבוהים.
לעומת זאת, חוסר רגישות יתאפיין בערכי PED נמוכים ויצביע על יכולת נמוכה לפתור את בעיית זיהוי איבר המקור.
צריך שיהיה ברור שהמרחב מיוצג על ידי אפס או אחד (=decision variables)
ושנתתי משקלים לפי תדירויות של מזג האוויר.

## Slide 19: Problem formulation - optimization
Objective 1:
Objective 2:
The basic model: Each combination (WS, WD, SC) is assumed to have a probability of to occur, such that . The Gaussian plume model is applied with all meteorological combinations, to obtain steady state solutions of pollution concentration maps. Each concentration map is given a weight according to the meteorological frequencies derived.
Methods
Notes: As the number of sensors |𝑅| increases, the PED values increases as well. Hence, maximizing the PED value conflicts with minimizing the number of sensors and the network’s cost.
Given that the deployment of a set of sensors is an expensive task due to sensors’ cost and maintenance, we may wish to minimize the number of sensors in use, and place them in a set of locations that together generate the highest PED value, which represents the best ability of those sensors to detect changes in industrial gas emissions. The first objective is then to minimize the number of sensors deployed
The discrete frequencies of each possible meteorological combination of wind speed (WS), wind direction (WD) and Pasquill–Gifford atmospheric stability class (SC). Each combination (WS, WD, SC) is assumed to have a probability of 𝑝 to occur, such that ∑1▒〖𝑝=1〗.
The Gaussian plume model is applied with all meteorological combinations, to obtain steady state solutions of pollution concentration maps. Each concentration map is given a weight according to the meteorological frequencies derived and so the average concentration map is generated to all sets of active/non-active combinations of sources.
For example, in the case of 5 sources, 31 options of 1-5 active sources exist, creating in total 355 possible combinations of two sets of active sources with different sizes {S}' and {S}". In this case, an array of 355 PED values are calculated for each optional solution. Out of 355 PED values, Number of 10 Categories of Transformation Pairs (NCTP) between same number of sources exist (1<->2 ,1<->3, etc.).

## Slide 20: Simulation setup
Simulated arena - A 1000x1000 m flat area
Showing:
1. Sources (red dots) with their average emission rates [kg s-1]
2. Optional sensor locations (black crosses)
3. Steady-state concentrations [], obtained by the Gaussian plume model for weather state of (WS, WD, SC) = (4 m s-1, 270 degrees, C class).
Preliminary results
Optional locations
Sources
Notes: An initial simulation setup was explored. A 1000x1000 m flat area was taken as the simulated arena, with sensors situated at ground level (i.e., z=0 in Eq. 1). Five point-sources (stacks) were arbitrarily given average emission rates of 0.47, 0.51, 0.38, 0.9 and 0.19 [kg s-1]. Figure 1 illustrates the simulation set with pollutant concentrations obtained by the Gaussian plume model for light (4 m s-1) west winds (270 degrees) and stability class C (slightly unstable). Sources are marked in red dots and optional locations of sensors are marked in black crosses. 396 optional locations were spread in a grid, 50 m apart, and at least 50 meters from the location of each source. Effective heights of stacks were taken at 10 m.
Hourly mean wind directions were binned into 8 categories (45 degrees each) and hourly mean wind speeds into 7 categories (<1, 1-2, 2-4, 4-6, 6-8, 8-10, >10 m s-1). With six possible Pasquill–Gifford classes for atmospheric stability (A-F), 336 weather states exist. The Gaussian plume model was applied with each weather state combination, using the mean value of each wind speed and direction category. For our initial simulation, we used 10-minutes wind data from Hadera-port station, obtained from the Israel Meteorological Service (IMS) for the years 2004-2018, to derive frequencies of each binned category (see Section ‎5.2.3). Figure 2 shows the windrose distribution of winds used in the initial simulation. The taken wind data are characterized by a bi-model distribution - comprised of west winds of relatively high speeds compared to east winds of lower speeds. The vector-average wind speed and direction is 0.9 m s-1 and 298 degrees, respectively. Scalar-average wind speed is 4.2 m s-1. Distribution of stability classes is as follows: A-1%, B-1%, C-6%, D-78%, E-11%, F-3%, as determined according to the 𝜎_𝐴 method (see Section ‎5.1.2).

## Slide 21: Data used for the simulation
Data obtained from IMS for Hadera-port station.
Preliminary results
Windrose distribution
Notes: An initial simulation setup was explored. A 1000x1000 m flat area was taken as the simulated arena, with sensors situated at ground level (i.e., z=0 in Eq. 1). Five point-sources (stacks) were arbitrarily given average emission rates of 0.47, 0.51, 0.38, 0.9 and 0.19 [kg s-1]. Figure 1 illustrates the simulation set with pollutant concentrations obtained by the Gaussian plume model for light (4 m s-1) west winds (270 degrees) and stability class C (slightly unstable). Sources are marked in red dots and optional locations of sensors are marked in black crosses. 396 optional locations were spread in a grid, 50 m apart, and at least 50 meters from the location of each source. Effective heights of stacks were taken at 10 m.
Hourly mean wind directions were binned into 8 categories (45 degrees each) and hourly mean wind speeds into 7 categories (<1, 1-2, 2-4, 4-6, 6-8, 8-10, >10 m s-1). With six possible Pasquill–Gifford classes for atmospheric stability (A-F), 336 weather states exist. The Gaussian plume model was applied with each weather state combination, using the mean value of each wind speed and direction category. For our initial simulation, we used 10-minutes wind data from Hadera-port station, obtained from the Israel Meteorological Service (IMS) for the years 2004-2018, to derive frequencies of each binned category (see Section ‎5.2.3). Figure 2 shows the windrose distribution of winds used in the initial simulation. The taken wind data are characterized by a bi-model distribution - comprised of west winds of relatively high speeds compared to east winds of lower speeds. The vector-average wind speed and direction is 0.9 m s-1 and 298 degrees, respectively. Scalar-average wind speed is 4.2 m s-1. Distribution of stability classes is as follows: A-1%, B-1%, C-6%, D-78%, E-11%, F-3%, as determined according to the 𝜎_𝐴 method (see Section ‎5.1.2).

## Slide 22: Optimization run
Preliminary results
Generation of Pareto frontier
Weights of recombination operators
Notes: להראות גם סרטון וגם גרפים שמראים התכנסות לסוג האלגוריתם.
Once all pre-calculations are obtained, the optimization process starts.
Technically, we assume that each location ω∈Ω may host a sensor. The decision variables are held in a data array, each value represents a sensor, linked to a certain location ω∈Ω. The sensor is “placed” in that location if the decision variable is 1 and is not “placed” if the decision variable is 0.
The Borg MOEA algorithm initiates its search by starting with a uniform random generation of its initial population of candidate solutions.
Then, the algorithm projects the set {𝑅} on Ω and evaluates all possible PED values of that set.
Then, based on the defined objectives, the Borg MOEA rewards those sets of decision variables (i.e., possible solutions) that dominate competing alternatives (i.e., better in all objectives) until a high-quality approximation of the Pareto frontier is attained.

## Slide 23: Obtained solutions
Each dot in the figure represents a non-dominated solution, i.e., an optimal solution for a given number of sensors.
The conflict between the cost of the network and its performance is reflected in the Pareto frontier - higher PED values and better network performance are achieved by larger number of sensors but result in a more expensive sensor array.
Preliminary results
Pareto frontier of two optimization runs
Notes: Figure 3. Pareto frontier of two optimization runs with two different PED-related objectives - 𝛹_(𝑚𝑖𝑛𝑖𝑚𝑎𝑙_𝑃𝐸𝐷). (blue) and 𝛹_(𝑝𝑒𝑟𝑐𝑒𝑛𝑡𝑖𝑙𝑒_𝑃𝐸𝐷) (red). Number of sensors were constrained to 2-300.
The optimization process was constrained to find the optimal locations of 2-300 sensors. Figure 3 illustrates the Pareto frontier received by two optimization runs, using the number of sensors (Ψ_(#r)) as the first objective (Eq. 6) and average minimal PED values (Ψ_(minimal_PED)) or the 25th percentile of all PED values (Ψ_(percentile_PED)) as the second objective (Eq.7 and Eq.8, respectively). The ultimate optimal solution in Fig. 3 would be the most upper left corner of the graph, which represents zero cost and highest PED. However, as this goal cannot be achieved due to the constraints of the problem, each dot in Fig. 3 represents a non-dominated solution (see Section ‎5.1.3), i.e., an optimal solution for a given number of sensors. The conflict between the cost of the network and its performance is reflected in the Pareto frontier - higher PED values and better network performance are achieved by larger number of sensors but result in a more expensive sensor array.

## Slide 24: Obtained solutions
a
b
c
e
d
f
Notes: Figure 7. Sample solutions for 2 (a), 4 (b), 5 (c), 7 (d), 8 (e) and 15 (f) sensors obtained from one optimization run, using number of sensors (𝛹_(#𝑟)) as the first objective (Eq. 6) and average minimal PED values (𝛹_(𝑚𝑖𝑛𝑖𝑚𝑎𝑙_𝑃𝐸𝐷)) as the second objective (Eq.7). Sources’ locations are marked in red dots and sensors’ locations in blue crosses. Average emission rate is specified next to each source [g m-3]. To the right of each displayed solution is attached a colormap of minimal PED values of each transformation pair between active sources.
Figure 7 (see Appendix C) shows several optimal solutions from one optimization run, using Ψ_(#r) as the first objective and Ψ_(minimal_PED) as the second objective. Solutions for relatively small number of sensors (low-cost networks) - 2, 4, 5, 7, 8 and 15 are displayed, in order to highlight the process of sensors’ deployment. It seems that preferable locations of sensors follow the highest derivative of the gas concentration in the air as these places are more sensitive to the nature of the source. This assumption will be tested in the suggested study. A colormap of minimal PED values of each transformation pair between each number of active sources are attached to each displayed solution. For example, in the colormap to the right of Fig. 7a, the minimal PED values of the transformation pairs 2<->5 and 1<->4 are around 3∙10^4 g m-3 (30 ppm). The higher the number of deployed sensors, the higher the minimal PED values.

## Slide 25: Obtained solutions
Preliminary results
Preferable locations and average concentration map
Preferable locations
Average concentration map
Notes: Figure 4. Preferable sensor locations, represented by the percentage of solutions each specific location was chosen, for two objectives - (a) average minimal PED values (172 solutions in total) and (b) 25th percentile of all PED values (167 solutions in total). Sources’ locations are marked in red dots and average emission rates are specified below. White areas are restricted locations, due to sources’ proximity.
For the above-mentioned obtained solutions, Fig. 4 displays a heatmap of preferable locations sensors were placed at. Each colored pixel on the 1000x1000 m simulation-map represents the percentage of solutions a sensor was placed at that specific location. It can be seen that the two objectives - Ψ_(minimal_PED) (Fig. 4a) and Ψ_(percentile_PED) (Fig. 4b) generate quite similar preferable locations, though some differences are seen; in Fig. 4a for example, the most preferable places (colored in dark blue) are between sources and as close as possible to a source. In Fig. 4b on the other hand, preferred locations are in between sources, but not necessarily as close as possible to them. These results are illustrated in order to show the process of finding a suitable objective function. An evaluation process of these solutions is further needed in order to determine which set of solutions performs better in measuring pollutant concentrations and detecting changes in emissions.

## Slide 26: Initial evaluation
26
Readings of optimal Vs. non-optimal solutions
Sampled solutions

## Slide 27: Summary and future research plan
Adequate monitoring of ambient air pollution is needed, among others, for regulation on industrial activity
We offer to design and develop a decision-making tool for an optimal deployment in time and in space of heterogenous sensor array, using a multi-objective optimization model, coupled with an air pollution dispersion model
The basic model considers the time varying meteorological conditions (wind velocity and atmospheric stability) and uses as the main objective a quantitative measure of the complexity of the given set of sources/sensors geometries: the Pairwise Euclidean Distance (PED) between the sensor network potential readings of different number of active sources.
Future modules will focus on the development of a temporal optimization module that allocates sensors with minimal transfer effort and on combining the two modules together.
Other aspects will be considers: various sources/sensors configurations, weather conditions and emission rates, heterogenous network, case-study of real-world
Thanks for listening…

## Slide 28: References
P. S. Kanaroglou et al., “Establishing an air pollution monitoring network for intra-urban population exposure assessment: A location-allocation approach,” Atmos. Environ., vol. 39, no. 13, pp. 2399–2409, 2005.
A. E. Eiben and J. E. Smith, Introduction to evolutionary computing, 2nd Editio., vol. 53. Springer, 2007.
D. Hadka, “Borg : An Auto-Adaptive Many-Objective Evolutionary Computing Framework,” vol. 21, no. 2, pp. 231–259, 2013.
D. Hadka, “Beginner ’ s Guide to the MOEA Framework,” p. 214, 2017.
C. D. Ahrens and R. Henson, Meteorology Today: An Introduction to Weather, Climate, and the Environment, 12th ed. Cengage Learning, Inc, 2017.
A. Boubrima, W. Bechkit, and H. Rivano, “Optimal WSN Deployment Models for Air Pollution Monitoring,” IEEE Trans. Wirel. Commun., vol. 16, no. 5, pp. 2723–2735, 2017.
J. D. Berman, L. Jin, M. L. Bell, and F. C. Curriero, “Developing a geostatistical simulation method to inform the quantity and placement of new monitors for a follow-up air sampling campaign,” J. Expo. Sci. Environ. Epidemiol., vol. 29, no. 2, pp. 248–257, 2019.

## Slide 29
Notes: Proove its not sorted

## Slide 30
Notes: See increasing number of sensors not necessarily add one in a new location, sometimes locations are changed