## Slide 1
Air pollution source term estimation
using self-adaptive Evolutionary multiobjective optimization
Shai Kendler#,1,2, Asaf Nebenzal3, David Gold4, Patrick. M. Reed4, Barak Fishbain1
Dept. of Environmental, Water and Agricultural Engineering, Faculty of Civil & Environmental Engineering, Technion – Israeli Institute of Technology, 2. Environmental physics department, Israel Institute for Biological Research, 3. Department of Mathematics, Technion – Israel Institute of Technology, 4. School of Civil and Environmental Engineering, Cornell University
# Corresponding authors: Prof. Shai Kendler - ikendler@gmail.com, Asaf Nebenzal - asaf.n@technion.ac.il
Results
Introduction
Acknowledgements
Summary & Conclusions
Methodology
What are Evolutionary Algorithms (EAs)?
Source term estimation
Research objective
What is a multi-objective optimization?
Objective-1: Minimize the difference between the sensors’ actual and computed readings:
Objective-2: Minimize the number of active sources (NAS):
This work presents a multiobjective scheme for estimating the source term in the case of multiple gas leaks.
The method consists of coupling self-adaptive Borg multiobjective evolutionary algorithm (MOEA) framework with a dispersion model, relying on the readings from a sparse network of sensors.
Two objectives are considered – minimizing the error of the estimated contamination level and the number of active sources, the letter corresponds to a simpler solution.
The method is tested in a simulated flat terrene with 0-9 sources, and results show the method is effective, with the main limitation being the number of sensors and their locations relative to the leaks.
A new measure to quantify the ability to resolve a specific configuration is presented – the PED criteria. This criteria, along with the findings of this work, will be used in future work to find the optimal deployment of sensors and their attributes.
A leak of various chemicals from industrial
activity may harm humans and the environment.
The first line of defense, before prioritizing any
mitigating steps, is detection of the resulted
plume and mapping the contamination level,
using a network of sensors.
Large number of sensors are typically needed for achieving concentration maps of high spatial and temporal resolution.
An alternative approach is to locate the leak source and flow rate (i.e., source term), and use it as input to an atmospheric dispersion model to generate spatial dense pollution maps.
Using simulations of a flat industrial site, our objective is to estimate the source term in the case of multiple leaks and a sparse network of sensors, using a state of the art evolutionary multiobjective search coupled with a Gaussian plume dispersion model.
More than one objective function is optimized simultaneously.
Tradeoffs exist between two or more conflicting objectives, for
example – error rate and cost (Fig. 2).
A Pareto frontier is the set of non-dominated solutions, being
chosen as optimal, if no objective can be improved without
harming at least one other objective.
Problem formulation
Inspired by biological Evolution, EAs are given a population of individuals ( = a set of candidate solutions) (Fig.3).
The environmental pressure causes natural selection and according to a fitness measure ( = objective function), the better candidates have a higher chance to survive and reproduce.
Recombination is applied to two or more selected parents ( = selected solutions) and results in one or more offsprings ( = new solutions) that may undergo a mutation.
Based on their fitness, the offsprings compete with the old candidates for a place in the next generation.
The process is iterated until a candidate with sufficient quality ( = a non-dominated solution) is found.
Figure 3. A general scheme of an Evolutionary Algorithm
Figure 5. Pareto frontiers calculated for the “Co9/9” arrangement for several .
Figure 6. A comparison between the calculated and the actual leak rate in Co9/9 arrangement for several .
Figure 7. Color map for calculated PED as a function of . a) “L9/9”, b) “Co9/9”, c) “Co9/6”, d) “L9/6”. High PED values presented in yellow color are a result of a large effect of NAS on the sensor network readings. Figures are truncated at , to allow comparison complex and simple situations
Figure 1. Example of a source and a network of sensor (﻿Hutchinson et. al., 2017).
Figure 2. Example of tradeoff between two objectives and the Pareto frontier
Non-dominated
Solution
Dominated
solution
Pareto frontier
Simulation set
600*600 m2 flat area, with constant west-wind (5 m/s) and slightly unstable conditions.
Leak rates of 0-1000 kg/s from varying number of leaks, between 0-9.
Leak heights of 5 m above ground level.
Six configuration sets, four of them are shown in Fig.4a-d.
Configuration “Co9/9“ (Fig.4a) is an arrangement of nine sources and nine sensors, each sensor located 50 m downwind from a leak.
Figure 4. Source-sensors arrangements. the term "source" refers to both active and non-active sources. a) ("Co9/9") - nine sources and sensors in a compact group, 50 m apart b) ("Co9/6”) - same as Co9/9, using six sensors, c) (”L9/6")- nine sources arranged in a line 50 m apart and a line of sensors 50 m downwind, sensors are 65 m apart, d) (”L9/9") same as ‘c’ using nine sensors, each sensor is in line with one of the sources.
Figure 5 shows the Pareto frontiers calculated by the Borg for the co9/9 arrangement, for an increasing number of leaks, .
The minimum is achieved for the correct number of leaks.
Figure 6 shows a comparison between the preset leak rates (at the 'x' axis) and the calculated leak rates (at the 'y' axis)
Excellent agreement is seen, due to the relatively convenient sensing configuration.
Scenario complexity estimation
PED = pairwise Euclidean distance for the sensor network observed readings between two sets of active sources with different sizes {S}’ and {S}”:
Figure 7 shows the calculated color maps of PEDs for of all configurations.
Figures 7a and b exhibit high PED values = simple scenarios
Figures 7c and d exhibit low PED values = complex scenarios

## Slide 2
Objective function
Objective
Configuration-1: “Co9/9“, Fig.4a
Configuration-2: “Co9/9“, Fig.4b
The method searches for a set of leaks; each one of them has a typical emission rate and location. The optimal set results in a minimal difference between the sensors’ actual and computed readings, while maintaining a minimum number of active sources.
computations were performed in a simulated a 600*600-meter flat area, with constant west-wind and C5 atmospheric stability class. Leak rates are 0-1000kg/s from varying number of leaks, between 0-9. Leaks height was 5 m above ground level. To gauge the air-pollution, a sparse WDESN is deployed in several configurations relative to the leaks.
The method searches for a set of leaks; each one of them has a typical emission rate and location. The optimal set results in a minimal difference between the sensors’ actual and computed readings, while maintaining a minimum number of active sources.