## Slide 1
Air pollution source term estimation
using self-adaptive Evolutionary multiobjective optimization
Shai Kendler#,1,2, Asaf Nebenzal3, David Gold4, Patrick. M. Reed4, Barak Fishbain1
Dept. of Environmental, Water and Agricultural Engineering, Faculty of Civil & Environmental Engineering, Technion – Israeli Institute of Technology, 2. Environmental physics department, Israel Institute for Biological Research, 3. Department of Mathematics, Technion – Israel Institute of Technology, 4. School of Civil and Environmental Engineering, Cornell University
# Corresponding authors: Prof. Shai Kendler - ikendler@gmail.com, Asaf Nebenzal - asaf.n@technion.ac.il
Results & Discussion
Introduction
Acknowledgements
Conclusion
Methodology
What are Evolutionary Algorithms ?
Source term estimation
Research objective
What is a multi-objective optimization ?
The method searches for a set of leaks; each one of them has a typical emission rate and location. The optimal set results in a minimal difference between the sensors’ actual and computed readings, while maintaining a minimum number of active sources.
The method was tested in a simulated 600m2 flat terrene with 0-9 sources. The results show that the method is effective, and the main limitation is the number of sensors and their locations relative to the leaks.
multiobjective optimization allows decision makers to simultaneously optimize across multiple performance criteria discover sets of optimal tradeoffs.
A leak of various chemicals from industrial activity may harm humans and the environment.
The first line of defense, before prioritizing any mitigating steps, is detection of the resulted plume and mapping the contamination level, using a network of sensors.
Large number of sensors are typically needed for mapping of high spatio-temporal resolution.
An alternative approach is to locate the leak source and flow rate (i.e., source term), and use it as an input for an atmospheric dispersion model to generate spatial dense pollution maps.
A careful deployment of a network of sensors can provide an accurate depiction of the contamination levels in the field.
Using simulations of a flat industrial site to estimate the source term in the case of multiple leaks, using a state of the art evolutionary multiobjective search coupled with a Gaussian plume dispersion model.
multiobjective optimization allows decision makers to simultaneously optimize across multiple performance criteria discover sets of optimal tradeoffs.
Simulation set
we wish to find the best combination of elements that maximizes some fitness function
fitter members will survive and proliferate, while unfit members will die off and not contribute to the gene pool of further generations, much like in natural selection.
Figure 2. A general scheme of an Evolutionary Algorithm
Figure 1. Example of tradeoff between two objectives and the Pareto frontier
Nondominated
Solution
Dominated
solution
Figure 3. Source-sensors arrangements.
d
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
a
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
b
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
N
c
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
e
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
f
Source
Sensor
Figure 4. Pareto frontiers calculated for the Co9/9 arrangement for several .
Figure 5. Pareto frontiers calculated for the Co9/9 arrangement for several .
Figure 6. Pareto frontiers calculated for the Co9/9 arrangement for several .